## Slide 1: INF0 341 Network Basics – LANs, WANs, & DMZs
By
Bob Larson

## Slide 2: Topics Covered
Basic Design of LAN and the Internet
LAN Addressing and Delivery
Gateway Router or Firewall
Address Resolution Protocol (ARP)
DHCP (Dynamic Host Configuration Protocol)
DNS (Domain Name Service)
NAT (Network Address Translation)

## Slide 3: Basic Design of LAN and the Internet
LAN – Local Area Network
  Belongs to single entity
  Typically uses private IP addresses
  Relatively safe
  Uses MAC (L2) address to communicate
Public Networks
  No entity owns or controls
  Requires public (real) IP addresses
  Relies on trust for compliance (?)
  Uses IP addresses to locate devices
    Still uses Layer 2 addresses for delivery
DMZ – Demilitarized Zone
  Owned by the LAN entity
  Accessible from inside or outside LAN
    Outside facing servers (Public)
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Web Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN

## Slide 4: LAN Addressing and Delivery
Typically Ethernet
Single Network LAN
  All devices share same IP address pool
    Same Network ID and Subnet mask
    Example: 10.0.0.0/24
Multiple Network LAN
  More than one IP address pool
  Router or L3 switch for inter-LAN exchanges
Switches (L2) and A/Ps pass-through
  Only need IP addresses for management
All data frames delivered via MAC (L2)
  Uses ARP to resolve IP to MAC addresses
Default Gateway to access outside world
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Web Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN

## Slide 5: Gateway Router or Firewall
Gateway connects LAN to outside world
  Inside part of LAN shares that IP address pool
  Outside public address typically from ISP
    Could connect to home office for Internet (rare)
Connect to DMZ (optional)
  A secure design for publicly shared servers
  These servers are often outsourced now
Can provide these services to LAN
  DHCP* to assign user IP addresses
  DNS* to convert URLS to IP address
  NAT to allow users go out into the Internet
  NTP* to provide synchronized time
  VPN encrypted links to remote public sites
  Controlled access to DMZ
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Web Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN
* Could be performed by servers

## Slide 6: Address Resolution Protocol (ARP)
Maps IP addresses to MAC addresses
MAC address is used by Ethernet to deliver frames in the local segment
IP Address identifies network ID (197.15.22.0 / 201.100.101.0) and host ID
Used to move packets from network to network
Internet
1

## Slide 7: ARP (Address Resolution Protocol)
LANs use only Ethernet MAC address for delivery
Routers use IP addresses to find the network to forward data to
ARP maps network address (IPv4) to a MAC address
Defined by RFC 826 in 1982
Use ARP requests (broadcast) to find an IP address, learns MAC from reply
Each connected device maintains ARP table of results
Note: Not the same as CAM table in a switch
On a Computer, Smartphone, etc.
On a Switch with IP management

## Slide 8: DHCP (Dynamic Host Configuration Protocol)
Used in IPv4 networks to assign IP address
  Plus other configuration information
    Default gateway, domain name, DNS servers, and time servers (NTP)
    Also supplies information for IP phones and other technologies
Eliminates the need for manual configuration
  Particularly important with mobile devices that come and go
Router or firewall device can act as DHCP server
  Larger networks administered by one or more DHCP server(s)
New device issues a DHCP request broadcast
  After brief exchange server provides the configuration information
  Issued as a renewable lease so that inactive addresses are recaptured

## Slide 9: Configuration Supplied by DHCP

## Slide 10: DNS (Domain Name Service)
Hierarchical decentralized naming system
  For computers, services, or other resources
  On the Internet or a private network
Translates easy to remember domain names to IP addresses
Worldwide, distributed service essential to the Internet
Provides redundancy
  No single point of failure
  It scales well
Been in use since the 1980s
URL: http://iSchool.uw.edu Email Account: BobLarson@uw.edu
Subdomain
Domain Name
Domain Name
Mail Box

## Slide 11: DNS Example
Device sends request to Local or ISP DNS Server for domain name only
If server doesn’t recognize
  It forwards request upstream
When IP is returned
  Each DNS handling the request adds it to its database
  Assumes if you asked once, you will likely ask again in the near future

## Slide 12: DNS Structure
For each country
EDU
MIT
WSU
UW
…
LAW
iSchool
MBA
…
Top Level Domain (TLD)
Second Level Domain
Subdomain
iSchool.uw.edu
http://iSchool.uw.edu
Original TLDs
  Com
  Org
  Net
  Int
  Edu
  Gov
  Mil

## Slide 13: NAT (Network Address Translation)
Replace a frame’s IP configuration with another
Switch a private IPv4 address with a global IP
  To go on the Internet
  Private addresses could preserve global IPs
  Private IPs are free, global addresses cost money
Global IP can come from
  A pool supplied by your ISP or
  The outside interface of the NAT router or firewall
NAT device maintains a NAT translation table
  To direct returning traffic to appropriate inside host
NAT provides a level of anonymity for inside hosts
  Typically connections must originate from inside the local network
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN

## Slide 14: NAT (Network Address Translation)
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN
.100 to Router
Router to Server
Server back to Router
Source & Destination IP & Ports Reverse

## Slide 15: Fin…