## Slide 1: INF0 341 Switching Loops
By
Bob Larson

## Slide 2: Topics Covered
Good, Bad, and Ugly of Redundancy
What is a Switching Loop or Bridge Loop?
Spanning Tree Protocol (STP)*
Another Look
Ensuring Network Availability with VLANs
A Network Topology Change

## Slide 3: Good, Bad, and Ugly of Redundancy
Newer switched networks include redundant links to increase reliability and reduce single points of failure.
With that comes the potential for data loops.

## Slide 4: What is a Switching Loop or Bridge Loop?
Loop will occur any time there is a redundant path or loop in the Layer 2 network

## Slide 5: Spanning Tree Protocol (STP)*
Loops are prevented by blocking the redundant path
Uses Spanning Tree Algorithm
Blocked link opens up if forwarding link fails
* IEEE 802.1D Standard

## Slide 6: Another Look
No loops
Lots of single point failures
Lots of loops – looping will occur
CAM Table or MAC address flapping
Broadcasts trigger both
Router
4th Floor
Core 1
3rd Floor
2nd Floor
1st Floor
A
1 of 45
Traditional Design
Router
4th Floor
Core 1
3rd Floor
Core 2
2nd Floor
1st Floor
A
1 of 45
Redundancy Design
* CAM entries time out after 300 seconds inactive

## Slide 7: Ensuring Network Availability with VLANs
We want redundancy in LANs
  To avoid orphan networks
  To ensure availability
Spanning Tree
  Blocks redundant link
With VLANs
  Each link can forward one VLAN
    Block the other

## Slide 8: A Network Topology Change
Topology Change
  Added device
  Failed link or device
STP Election
  Devices share BPDUs
  Select blocked link(s)
  Occurs automatically
  Can be programmed
    To control outcome
Bridge Protocol Data Unit (BPDU) – Data message transmitted across a LAN to detect loops in network topologies.

## Slide 9: Fin…