## Slide 1: INFO 341 Router and Routing Basics
By
Bob Larson

## Slide 2: Topics Covered
What is a Router?
What are the Router’s Roles?
What is a Route Table?
What are the Router Processes?
Directly Connected Networks
Static Routes
Default Routes (form of Static route)
What is a Routed Protocol?
What is a Routing Protocol?
Categories of Routing Protocols
Static vs. Dynamic Routing

## Slide 3: What is a Router?
Connects two or more networks
  Forwards traffic between the networks
At the edge Router or Firewall
  Connects LAN(s) to the outside world
  Is the Default Gateway out of the network
Within the LAN Router or Layer 3 switch
  Switch can segment a network (VLANs)
  Allows network segments to communicate
Network routers can exchange route info
  Bigger networks or multiple locations
  Only learns the organizations networks
    Not the Internet or ISPs
  Involves a routing protocol like OSPF
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Web Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN

## Slide 4: What are the Router’s Roles?
Forward data packets between networks
  By having at least two interfaces in different networks
  As data packet comes in one of the interfaces
    Router reads the destination IP address
    Using info from its route table
    It forwards packet to the next router
  Packet is forwarded router to router until it reaches its destination
Provides a broadcast and IP address boundary
  While switches forward broadcasts, routers don’t
It is the gateway or edge of the network
  All LAN hosts send packets through it to outside
  It should never have the same network connected to two interfaces
WiFi Access Point
Router or Firewall
Switch
Company LAN
Internet
Web Server
File Server
10.0.0.1/24
.5
.6
.100
.121
.113
.170
.111
.115
.180
.159
Web Server
Email Server
.9
.10
DMZ
Web Server
1.1.1.10
LAN – Private Network (Private IPs)
1.2.2.2
Public Network (Public IPs) WAN

## Slide 5: What is a Route Table?
A directory of all the organization’s networks known to the router
  Only the best path to each network is included
  Traffic to any unknown networks is discarded
  1st column letter indicates how it was learned (added)
    C – is a directly connected network
    S – is a Static route
    O – learned via OSPF routing protocol (use the legend)
Legend
All Known Networks
Router1#show ip route Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 E1 - OSPF external type 1, E2 - OSPF external type 2 i - IS-IS, su - IS-IS summary, L1 - IS-IS level-1, L2 - IS-IS level-2 ia - IS-IS inter area, * - candidate default, U - per-user static route o - ODR, P - periodic downloaded static route Gateway of last resort is not set D 192.168.11.0/24 [90/284160] via 192.168.1.1, 00:04:19, FastEthernet0/0 O 192.168.10.0/24 [110/11] via 192.168.2.1, 00:01:01, s0/0 R 192.168.9.0/24 [120/1] via 192.168.4.1, 00:00:07, s0/1 C 192.168.5.0/24 is directly connected, FastEthernet0/1 C 192.168.1.0/24 is directly connected, FastEthernet0/0 S 192.168.3.0/24 [1/0] via 192.168.1.1

## Slide 6: What are the Router Processes?
To build the Routing Table (Routing Process)
  Each routing protocol (if more than one) uses metrics to select best route to each known network
  Administrative Distance is used to decide if more than one method offers a route to same network
    Methods are Directly Connected, Static and Routing Protocols
  Longest prefix goes in first
To use the Routing Table (Forwarding Process)
  Forwarding process requests routes from Route Table
    First match in table is selected
    If no match, the packet is discarded
  Forwarding process builds OSI Layer 3 header and forwards to Layer 2

## Slide 7: Route Table Details
D 192.168.11.0/24 [90/284160] via 192.168.1.1, 00:04:19, FastEthernet0/0 O 192.168.10.0/24 [110/11] via 192.168.2.1, 00:01:01, serial0/0 R 192.168.9.0/24 [120/1] via 192.168.4.1, 00:00:07, serial0/1 C 192.168.5.0/24 is directly connected, FastEthernet0/1 C 192.168.1.0/24 is directly connected, FastEthernet0/0 S 192.168.3.0/24 [1/0] via 192.168.1.1
Source code – how was the route learned (added)
Network Address of a known network
Prefix Mask indicating the size of the network. 1st one is 24-bits or 255.255.255.0
Administrative Distance (AD) – indicates trust level, smaller numbers more trusted
  Note C (directly connected has an AD of 0, most trusted, and no metric)
  If there were two routes to 192.168.11.0 from different protocols, this one was trusted more and used
Metric used by the route method in column 1 – not relevant to compare to others
  If there were two routes to 192.168.11.0 using same protocol (D EIGRP), this one had smallest metric
Next-Hop router address traffic has to go to, to get to the destination network
  It means that adjacent router knows how to get to the destination and will forward the packet
How long since the last routing update – relevance depends on routing protocol
  Routes can be dropped if too long since last update on some like RIP
  Longer times indicates route stability for Link State protocols like OSPF
Interface on this router it goes to the get to the next-hop
  Static is like a direct order, i.e. follow the path to 192.168.1.1 and the next device will forward you
1
2
3
4/5
6
7
8

## Slide 8: Directly Connected Networks
They are all local networks for the router
No route configuration required, as long as:
  The interface is properly configured
  Not shut down, and
  Connected to a live link (Ethernet or serial device)
No routing protocol (OSPF) used
Since they appear in the table we know:
  They are directly connected (local) networks
  Which interface they are connected to
  We can send packets to those networks
D 192.168.11.0/24 [90/284160] via 192.168.1.1, 00:04:19, FastEthernet0/0 O 192.168.10.0/24 [110/11] via 192.168.2.1, 00:01:01, serial0/0 R 192.168.9.0/24 [120/1] via 192.168.4.1, 00:00:07, serial0/1 C 192.168.5.0/24 is directly connected, FastEthernet0/1 C 192.168.1.0/24 is directly connected, FastEthernet0/0 S 192.168.3.0/24 [1/0] via 192.168.1.1

## Slide 9: Static Routes
Manually configured by Admin
  The syntax is:
    ip route dest-ip-addr dest-mask [next-hop-ip | outbound-interface]
  Two examples:
    ip route 192.168.3.0 255.255.255.0 192.168.1.1 (next-hop-ip)
    ip route 192.168.3.0 255.255.255.0 Fa0/0 (outbound-interface)
  Because of AD (1) can be used to over-rule learned route
Example: All traffic for network 192.168.3.0/24 will be sent via the router at 192.168.1.1
  Only appears if link to 192.168.1.1 is in the table (up)
D 192.168.11.0/24 [90/284160] via 192.168.1.1, 00:04:19, FastEthernet0/0 O 192.168.10.0/24 [110/11] via 192.168.2.1, 00:01:01, serial0/0 R 192.168.9.0/24 [120/1] via 192.168.4.1, 00:00:07, serial0/1 C 192.168.5.0/24 is directly connected, FastEthernet0/1 C 192.168.1.0/24 is directly connected, FastEthernet0/0 S 192.168.3.0/24 [1/0] via 192.168.1.1

## Slide 10: Default Routes (form of Static route)
Important static route, or gateway of last resort
  Used to forward traffic for all unknown networks
    Usually to the ISP, who will forward or discard
    It means our routers only need to know about our networks
Manually configured by Admin
  The syntax is: 0.0.0.0 (any network) 0.0.0.0 (any mask)
    ip route 0.0.0.0 0.0.0.0 [next-hop-ip | outbound-interface]
  Two examples:
    ip route 0.0.0.0 0.0.0.0 10.1.0.2 (next-hop-ip)
    ip route 0.0.0.0 0.0.0.0 s0/1 (outbound-interface)*
  Because of AD (1) can be used to over-rule learned route
Gateway of last resort is not set
D 192.168.11.0/24 [90/284160] via 192.168.1.1, 00:04:19, FastEthernet0/0 O 192.168.10.0/24 [110/11] via 192.168.2.1, 00:01:01, serial0/0
Means none was created
Before:
* Should be used only with point-to-point connections, which is the norm for ISP connections.
Gateway of last resort is 10.1.0.2 to network 0.0.0.0 C 10.1.0.0/30 is directly connected, s0/1 S* 0.0.0.0/0 [1/0] via 10.1.0.2
Always the last entry
After:
Small networks have directly connected and a Default route

## Slide 11: What is a Routed Protocol?
Also referred to as routable protocol
Refer to data and address protocols
The addresses have a network ID
  Tells where to find the host (What network)
  IPv4 and IPv6 are examples
Earlier protocols had no network ID
  Only identified host in a broadcast domain
  Ethernet and MAC addresses are examples
  Earlier ones used host (computer) names

## Slide 12: What is a Routing Protocol?
Used by routers to exchange network info
  How routers learn where networks can be reached
  Can quickly adapt to network changes
    New networks or link outages
  Dynamic alternative to Static routing
    Routes manually configured by an Admin
    Must be reconfigured with every network change
Must be done before router can forward data
Does not forward data
  It provides the map routers use to forward data
  It allows Routed (routable) data to be forwarded

## Slide 13: Categories of Routing Protocols
Could be BGP or Static Route
Interior Gateway Protocol (IGP)
  Used within an Autonomous System (AS)
    AS is a company (Boeing) or organization (UW or US Army)
    Many examples RIP, OSPF, EIGRP, etc.
Exterior Gateway Protocol (EGP)
  Used within the Internet (Backbone)
    Only one Border Gateway Protocol (BGP)
  Only big AS can get direct BGP connection

## Slide 14: Types of IGPs
Distance Vector Protocols (example RIP)
  Original, older, routing protocols
  Measured distance in hop counts (metric)
    How many routers to the destination
    Smaller the hop count always chosen (A>C over A>B>C)
    Ignored link speed (bandwidth)
Link State Protocols (example OSPF)
  Uses metrics that factor in bandwidth
    Smallest metric chosen, fastest route (A>B>C over A>C)
    Less likely to pick a sub-optimal route
  Converges faster than DV after network changes
    All routers agree on changes and ready to forward data

## Slide 15: Static vs. Dynamic Routing
Benefits of static routing include:
  Less overhead on the router’s CPU
    No need to compute routes for the table
  No bandwidth usage – No route advertisements need to be sent
    Critical on low bandwidth links like serial T1s or Satellite links
    On backup links – Only appear when link is up. Don’t keep link up.
  Improved granularity more detailed control over route selection
  Security – routes can’t be tampered with by outsiders
Disadvantages of static routing include:
  Changes are labor intensive – a manual process
  Doesn’t scale well – Larger the network, the more difficult it is
    More Layer 3 devices, the more difficult static routing becomes
  Fault tolerance / fail-over becomes tricky
    Requires a thorough understanding of the network by Admin
    Disruptive outages can hurt performance and hard to work-around

## Slide 16: Fin…