## Slide 1: INFO 341 IP Network Design Ideas
By
Bob Larson

## Slide 2: Topics
Design Build Operate (DBO)
Why do we subnet?
Small Example
Large Example
SeaMobile Example
Getting Started
Tools Like PingPlotter

## Slide 3: Design Build Operate (DBO)
A process and a mindset – build it like you’ll have to run it
Variations
  Design Build Operate Maintain
  Design Build Outsource (or somebody else’s problem)
  DevOps – Developers and Operations team up to design
What about security (and privacy) – where does it fit in
  What is wrong with treating it as part of Operations?
  What is wrong with not thinking about it at all?
One-Off Designs are hard to operate and hard to secure
  Higher labor involved, more resources, often impossible to do right
  Harder to learn, harder to master

## Slide 4: Why do we subnet?
To set up logical divisions (Departments or user types)
Improved network security
Improved network performance (fewer sharing network)
More or fewer IP addresses required per subnet
Assure bandwidth to certain traffic – Phones or Device admin
B - 120
C - 12
A - 50
Router
Could be:
Floors
Departments
Buildings
Locations
Regions
Cruise ships

## Slide 5: Small Example
Single location
Typically done with VLANs
Want to segment off one or more departments
  Security / Privacy – R&D from operating departments
    So what they are doing doesn’t impact operations
  Security / Legal – M&A from Sales departments (financial)
Segment off some access types
  Guest network – limit access to company resources
  WiFi from Wired network – less secure from more secure

## Slide 6: Large Example
Enterprise with regions and locations (maybe hundreds)
  Domestic
    East / Central / Northwest / Southwest / Canada
  Global
    Europe / Middle East / Asia / Africa / Latin America / South Pacific
  Maybe States or Countries in Each
    Maybe Cities within each
      Maybe multiple locations in each

## Slide 7: SeaMobile Example
Cellular and WiFi on Cruise Ships
Many Customers (Cruise Companies)
  One to many ships
    Different types – Cruise ships, Ferries, Yachts, an Island
    Vary in size – few hundred connects to thousands
  Mobile – they move around
    Some travel the globe or others a set route (ferries)
    Depend on Satellite connections – blind spots, rough seas
    System may need to be turned off near shore (use local services)
How to track and maintain service?

## Slide 8: Five simple steps to create your subnets
Figure out how many host subnets you need.
  Rank them largest to smallest.
How many host bits will be needed for the largest network?
Choose the subnet for the largest network.
Note the address range to use, so you don’t overlap later.
Repeat steps 2–4 for the next largest subnet until done.
B - 120
C - 12
A - 50
Router
Each bit to right
  Doubles number of subnets (each with half the hosts)
Each bit to the left
  Doubles the number of hosts

## Slide 9: Getting Started
Think Big – You don’t want to do this again.
If there isn’t a design – start from the top
  What are your first level of summarizations
    Country, Region, etc. – Usually matches organizational reporting
  What is the next level – size requirements, and number of units
Each level needs to be big as the sum of all parts
For multi-similar locations (think Taco Times, Retail stores)
  Try to standardize Host octets (all routers .01, Main switch .03, etc)

## Slide 10: Simple National Example
Four Regions – East, West, North, South
Regions by State
X = 0-15 East, 16-31 West, 32-47 North, 48-63 South
  17 = Washington
  18 = Oregon
  19 = California
Y = Locations in the State (City, Store #, Acct Code)
  10.17.01 = Burien store
10.x.y.z

## Slide 11: Sample Ship Networks
IP address indicates type of use, location and device
Each rack devices would have unique IP addresses
No limit on access method
  Whatever the devices supports
No more NAT except devices requiring public IPs
Whisper
10.158.165.0 (254 addresses) NAT Ericsson
Cloud
10.158.164.0 (254 addresses) NAT Ericsson
Shadow
10.158.163.0 (254 addresses) NAT Ericsson
Carthage
10.198.52.0 (254 addresses) NAT Ericsson
Insignia
10.158.108.0 (254 addresses) NAT Ericsson
Diamond
10.158.120.0 (254 addresses) NAT Ericsson
SeaMobile

## Slide 12: Address Creation
Address Ranges (Coordinated with MTN)
  10.10.10.Y – SeaMobile Corporate
  10.158.X.Y – Cruise ships (8 = SeaMobile address, x = MTN’s ship ID)
    10.154.X.Y – Cruise ships WiFi VLAN 4 Passengers (x = MTN’s ship ID)
    10.155.X.Y – Cruise ships WiFi VLAN 5 Crew (x = MTN’s ship ID)
  10.198.X.Y – Misc. ferries, island (x maps to MTNs ship numbering scheme)
    10.194.X.Y – Misc ships WiFi VLAN 4 Passengers (x = MTN’s ship ID)
  10.13.X.Y – All SeaMobile external nets
    10.13.1.0 -- CDMA Center
    10.13.13.0 -- T1 / Pt-to-Pt links
  10.200.X.Y – MTN Corporate
10.158.67.25
Device
Ship ID or Location
Usage (Office, ship, T1)

## Slide 13: Ship Architecture
Ship
IModem
Rack Router
10.198.52.241
10.198.52.242
10.198.52. 1
Rack Devices

## Slide 14: SeaMobile Ship Example (Habib)

## Slide 15: Tools Like PingPlotter

## Slide 16: Fin…